 [F4 BMS]
CHECK-LISTS & PROCEDURES
MIRAGE 2000-5

Author: Memorial76
Version: 1.0
Date: 26/09/2017

References:
- Check-list Mirage 2000-5 et -9 by 10.235 Aigles
- Mirage 2000-5 for FSX by Rolland "Rollus" Laborie
- DCS Guide Mirage 2000C by Chuck
- La Guerre vue du Ciel by Marc Scheffler
- Forum : Check-Six : http://www.checksix-forums.com/

License :

Legende:

To/From	Radio

1. Cockpit readiness

COMMAND	ACTION	KEY	OBSERVATION
EJECTION SEAT	Armed	Shft + E	Red RBF around joystick / Outside hangar only
AIR SOURCE	Norm
MASTER ARM	Safe		Central position
CAT SELECTOR	A/A ou Charge
CNI	Backup
SLATS	Auto		Positions are inverted, leave it on LOCK
S/CONES	Auto
EXT LIGHTS	Steady
TRIMS	All Centered
ENGINE CONTROL	PRI
NVG	Check	N

2. Before start-up

COMMAND	ACTION	KEY	OBSERVATION
BATTERIES	Main		2 clicks
FLASHLIGHT	On	Shft + S	By night
WARNING PANEL	Test		Hold
UHF	Both		2 clicks
UHF BACKUP CHANNEL	Select
AUDIO/COMMS	Adjust level
NAV LIGHTS	Bright
FORM LIGHTS	Bright		2 clicks
PARKING BREAK	Serré	LAlt + P
THROTTLE	Idle
COCKPIT	Closed	Ctrl +C

3. Engine start-up
COMMAND	ACTION	KEY	OBSERVATION
SHUT OFF VALVE	Closed
ENGINE FEED	On		White mark up
ANTI COLL	Bright
JFS	Start	Shft + J
RPM	Check		20.00%
THROTTLE	10%
IDLE DETENT	Engage	LAlt + I
THROTTLE	Idle
RPM	Check		70.00%
WARNING PANEL	Check		All off

4. After start-up

COMMAND	ACTION	KEY	OBSERVATION
INSTRUMENT LIGHTNING	As required
ECLAIRAGE CABINE	As required
FLASHLIGHT	Off	Shft + S	By night
RAD ALT	Standby		1 click
INS	Align
CNI	UFC
FCR	On
FCC	On
SMS	On
VTL	On
UFC	On
MAP & GPS	On		Both on one click
TGP	On
VOYANT PANNE	Acquit
SERVAL	On
ECLAIR	On		Flares
SPIRAL	On		Chaff
RDR	Standby		Counter-measures mode
HANDOFF	On
TANK SELECTOR	Wing or Norm
DATA CARTRIDGE	Load
HUD	Bright
HUD COLOR	Adapt	LAlt + H
To TOWER : Ask for QNH
BAROMETRIC ALTIMETER	Set
INS	Check		Ready
INS	Nav

5. Taxi
COMMAND	ACTION	KEY	OBSERVATION
LANDING LIGHTS	On	Shft + L
To TOWER : Ask to remove chocks
DIRAV	On	Shft + !
PARKING BREAK	Off	LAlt + P
BRAKES	Test	K
To TOWER : Request taxi
Rolling
THROTTLE	Idle	-
EJECTION SEAT	Armed	-	If starting in hangar
EXT LIGHT	Flash

Ground control with rudder : keys ';' et ':'

6. Threshold

COMMAND	ACTION	KEY	OBSERVATION
PARKING BREAK	On	LAlt + P
AIRBRAKE	Check	B	In
GOUVERNES	Check	-	Free
WARNING PANEL	Check	-	All off
FCR	Adapted		As required
HSD	Adapted		As required
ICP – STPT	Auto	PAVNUM 4 then ARROW RIGHT
To TOWER : Wind check

7. Runway

COMMAND	ACTION	KEY	OBSERVATION
Enter runway between 120" and 90" before scheduled take-off time
PARKING BREAK	Off	LAlt + P
CAP	Check		as QFU
RAD ALT	On
DIRAV	Off	Shft + !

8. Take-off
COMMAND	ACTION	KEY	OBSERVATION
From TOWER : Wait for take-off clearance
BRAKES	On	K
THROTTLE	100%	-
WARNING PANEL	Check		All off
BRAKES	Release	-
CHRONO	Start	PAV NUM 6 then +	ICP mode Time
THROTTLE	Full PC	-

À 80 kt : Check acceleration à 18 ft/s² (max weight), 26 ft/s² (clear)

Rotation speed:	130 kt (150 kt if loaded)	Angle: 10°

250 kt reduce throttle to 100%, (300 kt if loaded)

ABANDON DECOLLAGE (V < V1)

COMMAND	ACTION	KEY	OBSERVATION
THROTTLE	Idle
AIRBRAKE	Out	B
BRAKES	On	K
MANCHE	Full in
DIRAV	On		V < 40 kt
Leave runway as fast as possible

9. In flight

COMMAND	ACTION	KEY	OBSERVATION
LANDING GEAR D'ATTERRISSAGE	In	G	Climb > 0 & V< 260 kt
WARNING PANEL	Check		All off

Standard climb
- Throttle 100%
- Accelerate to 450 kt (Mach 0.9) while climbing
Interception climb
- Full PC
- Accelerate to 450 kt (Mach 0.9) while climbing
10. Fence-In

COMMAND	ACTION	KEY	OBSERVATION
ANTI COL	Off
NAV LIGHTS	Off
FORM LIGHTS	Off		2 clicks
MASTER ARM	ARM
JMR	On		As required
RDR	On		Mode Adapted
CMDS	Program		Adapted to threat
ECLAIR	Checked		On
SPIRAL	Checked		On
FUEL	Checked		Quantity
ACMI	On	F
RADAR	As required	Ctrl + R
ECLAIRAGE INSTRUMENTS	Off
ECLAIRAGE CABINE	Off

11. Fence-out

COMMAND	ACTION	KEY	OBSERVATION
ECLAIRAGE INSTRUMENTS	As required
ECLAIRAGE CABINE	As required
RADAR	Stand-by	Ctrl + R
RDR	Stand-by
JMR	Off
MASTER ARM	SAFE
FUEL	Checked		Quantity
ACMI	Off	F
ANTI COL	Bright
NAV LIGHTS	Bright
FORM LIGHTS	Bright		2 clicks

12. In flight refuel
Contact
COMMAND	ACTION	KEY	OBSERVATION
To AWACS : Request vector toTanker
TACAN	Channel selected
HSI MODE	TCN
RADAR	ULS
ANTICOL	Check		On
NAV LIGHTS	Check		On

Closing in

COMMAND	ACTION	KEY	OBSERVATION
ALTITUDE	- 1000 ft		from Tanker
MASTER ARM	Sim
DED	On
ICP	Bingo	List then 2
RADAR	Stand by
RDR	Stand-by
To TANKER : Request Refuel
Left wing position
REFUEL LIGHTS	On
From TANKER : Wait for pre-contact position clearance

Refueling

COMMAND	ACTION	KEY	OBSERVATION
Pre-contact position
From TANKER : Contact clearance
Contact

- End of refueling

COMMAND	ACTION	KEY	OBSERVATION
To TANKER : Refuel done
Right wing position
REFUEL LIGHTS	Off
RDR	On
RADAR	On
DED	Off
MASTER ARM	ARM

13. Approach

COMMAND	ACTION	KEY	OBSERVATION
To TOWER : Request approach
WARNING PANEL	Check		All off
FUEL	Check
ILS	On
ILS	Frequency		Adapted

Descent
- Throttle to idle
- Descent speed 300 kt

14. Down wind

- Speed : 190 kt
- Altitude : 1500 ft QFE
COMMAND	ACTION	KEY	OBSERVATION
LANDING GEAR D'ATTERRISSAGE	Out		V < 240 kt

15. Finale
- Speed: 190 kt
- Altitude : 900 ft QFE
- Incidence 10° à 14°
- Short finale : 170 kt
COMMAND	ACTION	KEY	OBSERVATION
LANDING GEAR D'ATTERRISSAGE	Check		Out

ABORTED LANDING
COMMAND	ACTION	KEY	OBSERVATION
AIRBRAKE	Check	B	In
THROTTLE	Full PC
MANCHE	Climb 10°
LANDING GEAR	In	G
To TOWER : Abort landing

16. Ground

COMMAND	ACTION	KEY	OBSERVATION
THROTTLE	Idle
AIRBRAKE	Out	B
BRAKES	On	K	V < 100 kt
DIRAV	On	Shft + !	V < 40 kt

17. Taxi

COMMAND	ACTION	KEY	OBSERVATION
LANDING LIGHTS	Check	Shft + L	On
AIRBRAKE	In	B
RAD ALT	Standby		1 click
EXT LIGHT	Steady
ILS	Off

18. Shut off

COMMAND	ACTION	KEY	OBSERVATION
PARKING BREAK	On	LAlt + P
LANDING LIGHTS	Off	Shft + L
DIRAV	Off	Shft + !
To TOWER : Install chocks
HUD	Off
HANDOFF	Off
RDR	Off
SPIRAL	Off
ECLAIR	Off
SERVAL	Off
TGP	Off
MAP & GPS	Off
UFC	Off
VTL	Off
SMS	Off
FCC	Off
FCR	Off
CNI	Backup
INS	Off
RAD ALT	Off
SHUT OFF VALVE	Open
ENGINE FEED	Off		White mark down
ANTI COLL	Off
NAV LIGHT	Off
FORM LIGHT	Off
AUDIO/COMMS	Volumes Off
POSTE UHF	Off		2 clicks
EJECTION SEAT	Disarmed
COCKPIT	Open
BATTERIE	Off		2 clicks
AIR SOURCE	Off

SYSTEMES

EMERGENCIES
COMMAND	ACTION	KEY	OBSERVATION
EJECTION	Activate	Ctrl + E	Hold
JETTISON LOAD	Jettison	Ctrl + A	Hold
FUEL	Dump	Ctrl + Q	Hold

Lightning
COMMAND	ACTION	KEY	OBSERVATION
NIGHTVISION	On/Off	N
SPOTLIGHT	On/Off	Shft + S

Radio
COMMAND	ACTION	KEY	OBSERVATION
AWACS	Open/Cycle	A
AILLIER	Open/Cycle	Z
ELEMENT	Open/Cycle	E
VOL	Open/Cycle	R
TOWER	Open/Cycle	T
RAVITAILLEUR	Open/Cycle	Y

Modes
COMMAND	ACTION	KEY	OBSERVATION
A-A		F5
A-G		F6
NAV		Shft + BckSpace

Navigation
COMMAND	ACTION	KEY	OBSERVATION
WAYPOINT	Next	X
WAYPOINT	Previous	W

ICP
DED KEY	KEY
1-ILS	PAV NUM 1
2-ALOW	PAV NUM 2
3	PAV NUM 3
4-STPT	PAV NUM 4
5-CRUS	PAV NUM 5
6-TIME	PAV NUM 6
7-MARK	PAV NUM 7
8-FIX	PAV NUM 8
9-A-CAL	PAV NUM 9
0-M-SEL	PAV NUM 0
ENT	PAV NUM Enter
RCL	PAV NUM .
NEXT	+
PREV	-
UP	RCTRL + ARROW UP
DOWN	RCTRL + ARROW DOWN
SEQ	RCTRL + ARROW RIGHT
RTN	RCTRL + ARROW LEFT
COM 1	F1
COM 2	F2
IFF	F3
LIST	F4
DED	*

RADAR AIR-AIR

COMMAND	ACTION	KEY	OBSERVATION
RADAR	On/Silence/Discrete	Ctrl + R
PORTEE	Increase	Ctrl + F1
PORTEE	Decrease	Ctrl + F2
ANTENNE	Low	Ctrl + F5
ANTENNE	Center	Ctrl + F6
ANTENNE	High	Ctrl + F7
MODES DOGFIGHT
MODE DOGFIGHT	Activate	D	Short range
MODE MSL OVRD	Activate	,	Long range
MODE DOGFIGHT	Quit	C
SUBMODE	Bore-sight	TMS UP
SUBMODE	20*30 / 10*60	TMS DOWN	20*30 = radar off
SUBMODE	Activate radar	TMS RIGHT	From 20*30 radar off
MODES BVR
MODE RWS
SUBMODE	SAM	TMS UP
SUBMODE	STT	TMS UP	On designated contact
MODE TWS
SUBMODE	SAM	TMS UP
SUBMODE	STT	TMS UP	On designated contact
LOCK		PAV NUM 0 / TMS UP
UNLOCK		PAV NUM . / TMS DOWN

MISSILES INFRA ROUGE

COMMAND	ACTION	KEY	OBSERVATION
MODE	DGFGT or MSL OVRD	D ou ,
REFROIDISSEMENT	On		COOL displayed on SMS
MISSILE	UNCAGED	U	Manual or auto (mode TD)
CIBLE	Locked
MISSILE	Release
Fox two

MISSILES RADAR

COMMAND	ACTION	KEY	OBSERVATION
MODE	A-A, DGFGT or MSL OVRD	F5, D or ,
DISTANCE	Check		In range
MISSILE	Release
Fox three

A : time to HPRF
M : time to MPRF
T : time to Interception
L : time left

CONTRE MESURES

COMMAND	ACTION	KEY	OBSERVATION
PROGRAMME	Activate	CMS UP = M
PROGRAMME 6	Activate	CMS LEFT = ;
PROGRAMME 5	Activate	S
FLARES	Release	$
CHAFFS	Release	^
JAMMER	Activate	J

PROGRAMME	UTILISATION
1	High and Middle altitude SAM
2	AA IR
3	AG Pop-up (Chaffs only)
4	Pop-up (Chaffs and Flares)
5	Unknown threat
6	Flares Only